Pointers to Members

---
- Pointers to Members:
  - Calling functions, calling member functions
  - Pointers to member functions
  - Small example using pointers to members

---
Calling a function:
- What's happening ?
  - 12 is pushed on the stack
  - the function is called:
    its RA is put on the stack
  - the argument follows the RA
void function(int x)
// called as:
function(12);
high addresses
...
12
RA
stack
growth
[Speaker Notes: RA: return address. The address where execution continues when the called function terminates.]

---
- Calling a function
  using a pointer to
  that function:
- What's happening ?
  - 12 is pushed on the stack
  - the function is called using the
    address found in fp: the
    function's RA is put on the stack
  - the argument is above the RA
void function(int x)
void (*fp)(int) = function;
// called as:
(*fp)(12);
...
12
RA
stack
growth

---
- Calling a member function: What happens?
  - 12 is put on the stack
  - function is called?
    - can't do this:
      how would function know
      for which object it's called?
void Class::function(int x)
// called for object obj:
obj.function(12);
...
12
RA
stack
growth
[Speaker Notes: Assume that the class has a member int d_value How would member know who's value we're referring to?]

---
- Calling a member function: What happens?
  - A hidden argument specifies the object:
void Class::function(int x)
// called for object obj:
obj.function(12);
// called as:
Class::function(&obj, 12);
...
12
&obj
RA
stack
growth

---
- Calling a member function:
  - Prototypes of class-members and class-less (free) functions differ
  - Can't assign the address of a member function to a pointer to a class-less (free) function:
void Class::function(int x);
// won't compile:
void (*fp)(int) = &Class::function ;
it's not just `function', it's
Class's function.
Hence: &Class::function

---
Defining a pointer to a member function:
  - fp is a pointer into Class, to a (non-static) member function of that class.
void Class::function(int x);
void (Class::*fp)(int) = &Class::function;
[Speaker Notes: At the same time: note how to obtain a member function's address and how to initialize the pointer.]

---
- Calling a member using a pointer to a member function:
  - requires an object.
  - where has the pointer been defined ?
void (Class::*fp)(int) = &Class::function;
Class object;
(object.*fp)(12);
[Speaker Notes: The pointer to a member may be defined (and for public members) initialized everywhere. Only calling the member through its pointer requires an object. Note the syntax: .* is an operator, indicating that a member is called using a pointer to a member. When a pointer to an object is available, use the ->* operator. E.g., Class *cp = &object; (cp->*)(12);]

---
Application: Subtractor class having members producing infix, prefix or postfix subtractions
class Subtractor	// showing part of the public
{	// interface
typedef std::string str;
enum Mode
{
PREFIX, INFIX, POSTFIX,
}
str prefix(str left, str right); // - 3 4
str infix(str left, str right); // 3 - 4
str postfix(str left, str right); // 3 4 -
};
[Speaker Notes: In `real life' situations the parameters should be std::string const &.]

---
- Define a function performing either pre- in- or postfix operations, on a local Subtractor object:
  - Using an if- or switch-statement:
    - complex, hard to maintain, relatively slow (switch eval.)
  - Using an array of function addresses and select using a Mode value
    - fast (but requires index calculation); where is the array?
  - Using a pointer to a member parameter
    - fastest, simplest, single evaluation.

---
Define a function performing either the prefix, infix or postfix operations, using a Subtractor object
void Subtractor::subtract(str (Subtractor::*fp)(str, str),
        str left, str right)
{
   cout << (this->*fp)(left, right) << endl;
}

---
Calling subtract for different Subtractor objects:
int main()
{
Subtractor prefix;
Subtractor postfix;
cout <<
prefix.subtract(&Subtractor::prefix, "4", "8") << '\n' <<
postfix.subtract(&Subtractor::postfix, "4", "8") << '\n';
// shows:
//	- 4 8
// 4 8 -
}
[Speaker Notes: When calling a member through a pointer from within a member function, an object is still required. If the object is the object which was used to call that member, then this is used to call the member function. E.g. (this->*infix)(arg1, arg2); Note the parentheses!]

---
- When to use pointers to members?
  - When classes offer features through members having identical prototypes
  - Only one feature will be selected once the program runs
  - Intuitive alternatives:
    - switches
    - arrays of pointers to members, using a selector index
[Speaker Notes: When calling a member through a pointer from within a member function, an object is still required. If the object is the object which was used to call that member, then this is used to call the member function. E.g. (this->*infix)(arg1, arg2); Note the parentheses!]

---
C++ Pointers to Members
That's All, Folks,
about
Pointers to Members.